APPENDIX B

ADJUSTMENTS TO CONSIDER TO MEET TIME AVAILABLE (TAvailable)

Adjustments are often based on evaluation of both limitations identified and resources available.  If TDetection is excessive, leaving little time for staff response or safe evacuation, then improvements in early detection should be considered.  On the other hand, if TAvailable is impacted by open room doors permitting early contamination of the corridor, then room detection devices and door self-closers in combination with hold-open devices should be considered to keep the corridor tenable as long as possible during floor or zone evacuation.

Adjustments to consider:

- increasing the number of supervisory staff on duty;

- enhancing supervisory staff training;

- incorporating more or different types of assistive devices;

- redistributing the placement of the occupants who require the greatest assistance in evacuation;

- reducing the overall number of patients or residents in the building or zone;

- reducing the flammability of furnishings within patient or resident bedrooms to reduce likelihood of ignition and limit fire growth;

- use of zone separation (fire compartments) to add additional points of safety on the floor area, which can reduce the occupant load in each zone and travel time to a point of safety and provide additional time for subsequent evacuation stages;

- enhancing early detection in various areas of the facility such to enable faster supervisory staff response to a fire; and

- installing fire protection systems such as sprinklers, which can effectively control a fire, thereby increasing the time available